## Slide 1: DETECTION OF HEDONIC RESPONSE USING BALLISTOCARDIOGRAPHY (BCG)
END Semester Presentation
Under the guidance of :-
Prof. U.S. Tiwari
Group members :
Praneel Rathore IIT2013034 Aayush Garg IIT2013061
Nipun Manocha IIT2013124

## Slide 3: INTRODUCTION
In this project, we aim to exploit subtle head oscillations that accompany the cardiac cycle to extract information about cardiac activity from videos.
The cyclical movement of blood from the heart to the head causes the head to move in a periodic motion. Our algorithm detects pulse from this movement.
The ballistocardiograph (BCG) is a measure of ballistic forces on the heart. Ballistocardiography is a technique for producing a graphical representation of repetitive motions of the human body arising from the sudden ejection of blood into the great vessels with each heart beat.
BALLISTOCARDIOGRAPHY

## Slide 4: PROBLEM
To develop a new technique which is to measure parameters associated with pulse rate (Heart Rate Variability) and in turn depicting change in emotions (positive/negative) using hedonic response.

## Slide 5: PROJECT OBJECTIVES
To develop contact-less, cable less, non-invasive and simple technique to measure important heart related parameters, Pulse Rate and Heart Rate Variability.
The technique should record pulse rate and Heart Rate Variability using head vibrations in video.
With the help of this technique, we should be able to classify the mood/emotion of a subject as positive or negative.
Positive = {fun, exciting, joy, happy, cheerful}
Negative = {sad, depressing, hate, sentimental, melancholy}

## Slide 6: TECHNOLOGY USED
Python 2.7
OpenCV 2.4.10
Scipy 0.18.1
Numpy 1.11.2
Matplotlib 1.5.3
PeakUtils 1.0.3

## Slide 7
METHODOLOGY

## Slide 8
Video
Face Classifier
Get Focused Area

## Slide 9
Video
Face Classifier
Get Focused Area

## Slide 10
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)

## Slide 11
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)

## Slide 12
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)

## Slide 13
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)

## Slide 14
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation

## Slide 15
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation

## Slide 16
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz

## Slide 17
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz

## Slide 18
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz
PCA to select the best component

## Slide 19
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz
PCA to select the best component

## Slide 20
We quantify a signal’s periodicity as the percentage of total spectral power accounted for by the frequency with maximal power and its first harmonic. And thus select the most periodic signal.

## Slide 21
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz
PCA to select the best component
Detect Peaks in Curve

## Slide 22
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz
PCA to select the best component
Detect Peaks in Curve

## Slide 23
Video
Face Classifier
Get Focused Area
Select Corner Points (Features to track)
Track Features (Lucas Kanade)
Cubic Spline Interpolation
Butterworth Bandpass Filter
(0.75, 5) Hz
PCA to select the best component
Detect Peaks in Curve
Compute BPM

## Slide 24
fs = sampling frequency
fpulse = max freq of the chosen signal
RR_intervals = [consc. detected peak distances]
pulseRate = 60 * fs / mean(RR_intervals)

## Slide 25
VERIFICATION OF PULSE RATE FINDINGS
Tested on self recorded videos
Calculated BPM from our algorithm was verified with the results of MI band that the subject was wearing at the time of recording.

## Slide 26
VERIFICATION OF PULSE RATE FINDINGS
Tested on self recorded videos
Calculated BPM from our algorithm was verified with the results of MI band that the subject was wearing at the time of recording.
71 BPM, 73 BPM, 75 BPM, …

## Slide 27
VERIFICATION OF PULSE RATE FINDINGS
Test 1
Tested on self recorded videos
Calculated BPM from our algorithm was verified with the results of MI band that the subject was wearing at the time of recording.

## Slide 28
CALCULATION OF HRV
HRV = fs / samples in one RR_interval
HRV for peaks 1 and 2 = 0.984615, sample distance = 130.000000
HRV for peaks 2 and 3 = 0.941176, sample distance = 136.000000
HRV for peaks 3 and 4 = 0.955224, sample distance = 134.000000
HRV for peaks 4 and 5 = 1.000000, sample distance = 128.000000
HRV for peaks 5 and 6 = 1.024000, sample distance = 125.000000
…

## Slide 30
We calculated HRVs for 11 subjects in the following moods –
POSITIVE – {fun, exciting, joy, happy, cheerful}
NEGATIVE = {sad, depressing, hate, sentimental, melancholy}

## Slide 31
FOR ANY 02 SUBJECTS
Negative emotions – Relatively More Right Skewed, mean > median

## Slide 32
FOR ALL SUBJECTS COMBINED
Central Limit Theorem

## Slide 33
Sub. No. | Statistical Measure | Positive 3.59, 8 |  |  |  |  | Negative 0, 6.65 |  |  |  |  | 
01 | Area under the curve | 36.16 |  |  |  |  | 42.03 |  |  |  |  | 
 | Standard Deviation | 0.26 |  |  |  |  | 0.255 |  |  |  |  | 
 | Skewness | -0.314 |  |  |  |  | -0.208 |  |  |  |  | 
 | Val Scale (Skewness) | 5.76 |  |  |  |  | 0.91 |  |  |  |  | 
 | Area for intervals (0.3) | 0.14 | 0 | 5.4 | 9 | 9 | 0 | 0.98 | 6.25 | 9 |  | 9
02 | Area under the curve | 25.50 |  |  |  |  | 32.009 |  |  |  |  | 
 | Standard Deviation | 0.282 |  |  |  |  | 0.287 |  |  |  |  | 
 | Skewness | 0.012 |  |  |  |  | -0.027 |  |  |  |  | 
 | Val Scale (Skewness) | 5.33 |  |  |  |  | 3.58 |  |  |  |  | 
 | Area for intervals (0.3) | 0 | 0.62 | 5.44 | 9 | 9 | 0 | 0.86 | 4.84 | 9 |  | 9
03 | Area under the curve | 31.888 |  |  |  |  | 53.369 |  |  |  |  | 
 | Standard Deviation | 0.231 |  |  |  |  | 0.345 |  |  |  |  | 
 | Skewness | 0.0756 |  |  |  |  | 0.697 |  |  |  |  | 
 | Val Scale (Skewness) | 4.79 |  |  |  |  | 3.76 |  |  |  |  | 
 | Area for intervals (0.3) | 0 | 2.95 | 6.65 | 9 | 9 | 0 | 2.41 | 6.08 | 8.11 |  | 9
04 | Area under the curve | 47.587 |  |  |  |  | 56.433 |  |  |  |  | 
 | Standard Deviation | 0.316 |  |  |  |  | 0.300 |  |  |  |  | 
 | Skewness | 0.738 |  |  |  |  | 0.889 |  |  |  |  | 
 | Val Scale (Skewness) | 3.59 |  |  |  |  | 0.0 |  |  |  |  | 
 | Area for intervals (0.3) | 3.55 | 0 | 7.34 | 8.41 | 9 | 2.96 | 0 | 7.70 | 8.53 |  | 9
05 | Area under the curve | 22.725 |  |  |  |  | 27.435 |  |  |  |  | 
 | Standard Deviation | 0.363 |  |  |  |  | 0.343 |  |  |  |  | 
 | Skewness | 1.046 |  |  |  |  | 1.081 |  |  |  |  | 
 | Val Scale (Skewness) | 5.4 |  |  |  |  | 6.65 |  |  |  |  | 
 | Area for intervals (0.3) | 0.24 | 0 | 8.27 | 9 | 8.51 | 0 | 0.55 | 8.44 | 9 | 8.63 | 

## Slide 34
Negative emotions – Relatively More Right Skewed, mean > median
Neg
Pos

## Slide 35
Thank you
Group members :
Praneel Rathore IIT2013034 Aayush Garg IIT2013061
Nipun Manocha IIT2013124